## Slide 1
ITU-ML5G-PS-007
Lightning-Fast Modulation Classification
With Hardware-Efficient Neural Networks
Aaronica Team
Mohammad Chegini [1] , Pouya Shiri [2] , Amirali Baniasadi [3]
International Telecommunication Union
Organized by Xilinx
[1] Shahid Beheshti University. mohammad.chegini@hotmail.com [2] University of Victoria. pouyashiri@uvic.ca
[3] University of Victoria. amiralib@uvic.ca

## Slide 2: Our Goal
Develop a Deep Neural Network (DNN)
  Target: Radio Frequency (RF) applications
  Extreme Throughput
  Ultra-Low Latency
  High Energy Efficiency
Example RF Application
  6G Communication Networks
  Modulation Classification

## Slide 3: Modulation classification (MC)
Modulation Classification
  A well-known problem in RF domain
  Requires high throughput and low latency
MC Applications
  Spectrum interference monitoring
  Radio fault detection
  Dynamic spectrum access
  Numerous regulatory and defense applications
Fig. Modulation Classification procedure
Notes: Reference: https://static-01.hindawi.com/articles/mpe/volume-2020/2678310/figures/2678310.fig.001.svgz

## Slide 4: DNN for Modulation Classification
DNNs are promising tools for analyzing raw data
Pros:
  Higher accuracy w.r.t conventional methods
  Automatic feature extraction
Cons:
  Design complications
  Computationally expensive
  Resource demanding (but we need high throughput and low-latency!)
Our objective: design a DNN specialized for RF domain applications
Fig. Comparison of conventional and proposed method
Notes: What is reference

## Slide 5: Evaluation metrics
In RF-Domain, we generally require hardware implementation.
H/W performance indices:
  FLOPs
  MACs

## Slide 6: Design Complications
Domain-specific DNN Design
  Choice of network architecture
  Network modifications:
    Type/Number of layers/filters
    Network compression techniques (Quantization, etc.)
First option: Exhaustive search
  Grid Search
  Evolutionary Algorithms (Genetic Algorithm, PSO, …)
  Neural Architecture Search (Using Reinforcement Learning, …)
  Time-Consuming and Resource Hungry for large Datasets (highly unpractical)
Notes: Grid search: https://www.oreilly.com/library/view/statistics-for-machine/9781788295758/e4dac91e-0078-4c8a-a44f-78a28abb649b.xhtml

## Slide 7: Problem statement
Minimize inference cost on the challenging and well known RadioML 2018 dataset
Minimum final accuracy: 56%
Solutions of Aaronica Team
Initial round: Pruning MobileNet
  Got 3rd place
Final round: AaronNet Network
  Designed a specialized DNN after the initial round

## Slide 8: Possible Architectures
VGG, Inception, ResNet, MobileNet, ShuffleNet
  Each networks has innovations to stand out
  MobileNet
Pointwise and depth-wise convolution
  Reducing the number of multiplications
  Higher throughput with lower computation cost
Notes: Mobilenet: https://towardsdatascience.com/review-xception-with-depthwise-separable-convolution-better-than-inception-v3-image-dc967dd42568

## Slide 9: AaronNet
Specialized for RF-domain
Group-Wise convolutions
Introducing Multi-Scale Convolutional (MSC) layer
Adaptive Max Pooling
Variations
  AaronNet32: 32 filters
  AaronNet48: 48 filters
AaronNet Architecture

## Slide 10: Optimizing AaronNet
Significant results using the following methods:
  Layer-wise quantization and pruning
  Using Self-attention mechanism SE block
  Unstructured pruning (More energy efficiency)
  Structured pruning (More hardware friendly)
The best results we had so far: Unstructured Pruning
  AaronNet+: Slightly pruned version of AaronNet while having the same accuracy as AaronNet
  AaronNet++: Pruned to it’s limit, while meeting minimum accuracy of competition
Finalizing our paper for submission
Notes: Spring: https://alexanderteachingstudio.com/dont-compress-yourself-improving-your-posture-by-doing-less/

## Slide 11: Results: Initial Round
MobileNet Architecture
Baseline for inference cost: VGG network
  Inference cost = 1
  Accuracy = 59.46%
Unstructured Pruning of MobileNet (initial round)
  Using P100 GPU on Kaggle
  Pruned 30% of the weights
  Accuracy = 56.15%
  21x inference cost improved (0.046)

## Slide 12: Results: Final Round
Higher is better

## Slide 13: Results: Final Round
Using A6000 RTX GPU
  Trained and pruned variations of AaronNet
Highest Accuracy: AaronNet48+
  Accuracy = 60.07%
  23x inference cost (0.04320)
Best Cost: AaronNet32++
  Acceptable accuracy 56.07%
  64x inference cost (0.01539)
Lower is better

## Slide 14: Results: Final Standing

## Slide 15: Questions