## Slide 1
ITU-ML5G-PS-007
Lightning-Fast Modulation Classification
With Hardware-Efficient Neural Networks
Aaronica Team
Mohammad Chegini [1] , Pouya Shiri [2] , Amirali Baniasadi [3]
International Telecommunication Union
Organized by Xilinx
[1] Shahid Beheshti University. mohammad.chegini@hotmail.com [2] University of Victoria. pouyashiri@uvic.ca
[3] University of Victoria. amiralib@uvic.ca

## Slide 2: Our Goal
Develop a Deep Neural Network (DNN)
  Target: Radio Frequency (RF) applications
  Extreme Throughput
  Ultra-Low Latency
  Highly Energy Efficiency
Example RF Application
  6G Communication Networks
  Modulation Classification

## Slide 3: Modulation classification (MC)
Modulation Classification
  A well-known problem in RF domain
  Requires high throughput and low latency
MC Applications
  Spectrum interference monitoring
  Radio fault detection
  Dynamic spectrum access
  Numerous regulatory and defense applications
Notes: Reference: https://static-01.hindawi.com/articles/mpe/volume-2020/2678310/figures/2678310.fig.001.svgz

## Slide 4: DNN for Modulation Classification
DNNs are promising tools for analyzing raw data
Pros:
  Higher accuracy w.r.t conventional methods
  Automatic feature extraction
Cons:
  Design complications
  Computationally expensive
  Resource demanding (but we need high throughput and low-latency!)
Our objective: design a DNN specialized for RF domain applications
Notes: What is reference

## Slide 5: Evaluation metrics
In RF-Domain, we generally require hardware implementation.
H/W performance indexes:
  FLOPs
  MACs
  Accuracy

## Slide 6: Design Complications
Domain-specific DNN Design
  Choice of network architecture
  Network modifications:
    Type/Number of layers/filters
    Network compression techniques (Quantization, etc.)
First option: Exhaustive search
  Grid Search
  Evolutionary Algorithms (Genetic Algorithm, PSO, …)
  Neural Architecture Search (Using Reinforcement Learning, …)
  Time-Consuming and Resource Hungry for large Datasets
Notes: Grid search: https://www.oreilly.com/library/view/statistics-for-machine/9781788295758/e4dac91e-0078-4c8a-a44f-78a28abb649b.xhtml

## Slide 7: Problem statement
Minimize inference cost on the challenging and well known RadioML 2018 dataset
Minimum final accuracy: 56%
Solutions of Aaronica Team
Initial round: Pruning MobileNet
  Got 3rd place
Final round: AaronNet Network
  Designd a specialized DNN after the initial round
  A potential network for RF domain applications
    Identification of RF-interference
    RF Fingerprint

## Slide 8: Possible DNNs
VGG, Inception, ResNet, MobileNet, ShuffleNet
  Each networks has innovations to stand out
  MobileNet
Pointwise and depth-wise convolution
  Reducing the number of multiplications
  Higher throughput with lower computation cost
Notes: Mobilenet: https://towardsdatascience.com/review-xception-with-depthwise-separable-convolution-better-than-inception-v3-image-dc967dd42568

## Slide 9: AaronNet
Specialized for RF-domain
Group-Wise convolutions
Introducing Multi-Scale Convolutional (MSC) layer
  Specialized for RF signal input
Adaptive Max Pooling
Variations
  AaronNet32: 32 filters
  AaronNet48: 48 filters
AaronNet Architecture

## Slide 10: Optimizing AaronNet
Significant results using the following methods:
  Layer-wise quantization and pruning
  Using Self-attention mechanism SE block
  Unstructured pruning (More energy efficiency)
  Structured pruning (More hardware friendly)
The best results we had so far: Unstructured Pruning
  AaronNet+  Slightly pruned AaronNet
  AaronNet++  Highly pruned AaronNet
Finalizing our paper for submission
Notes: Spring: https://alexanderteachingstudio.com/dont-compress-yourself-improving-your-posture-by-doing-less/

## Slide 11: Results: Initial Round
MobileNet Architecture
Baseline for inference cost: VGG network
  Inference cost = 1
  Accuracy = 59.46%
Unstructured Pruning of MobileNet (initial round)
  Using P100 GPU on Kaggle
  Accuracy = 56.15%
  21x inference cost improved (0.046)

## Slide 12: Results: Final Round
Highest Accuracy: AaronNet48+
  Accuracy = 60.07%
  23x inference cost (0.04320)
Best Cost: AaronNet32++
  Acceptable accuracy 56.07%
  64x inference cost (0.01539)
Using A6000 RTX GPU

## Slide 13: Results: Final Round

## Slide 14: Results: Final Standing

## Slide 15: Questions